A) Objectives
Re-familiarize ourselves with the launchpad and relevant concepts:
- Hardware and Software FIFOs
- UART, Serial I/O
- ST7735 LCD driver
- HW / SW Interrupts

We will write basic drivers and an interpreter for the basis of our OS.

B) Hardware Design (not assigned for lab 1)

C) Software Design
- LCD Driver (ST7735_.c and ST7735_.h)
- ADC Driver (ADC.c and ADC.h)
- Timer Driver (OS.c and OS.h)
- Interpreter (main.c)

D) Measurement Data
  1) 38 cycles @ 80MHz = 475 ns. We estimate the number of cycles within the interrupt routine by counting the number of instructions. (27 instructions)
  2) 1.320 us = 106 cycles @ 80MHz. To measure the total time, we toggled pins in both the main program and in the timer interrupt. This allowed us to trigger the oscilloscope at the correct time to see when the pin stops toggling in the main program.

E) Analysis and Discussion
  1) Range = 0 to 3.3 V. Resolution = 4096. Precision = 0.8 mV (3.3/4096).
  2) Software-triggered interrupts (start the interrupt in the user program), and timer-triggered (use systick or another system timer)
  3) Our estimate is based on the first method by toggling a pin. However, the second method is more accurate because we can also measure the time taken by the hardware to push and pop registers to service the interrupt. We were able to do the second method by triggering within the ISR and looking the time when the main program stops toggling another LED.
  4) 1.320us / 27 instructions = 48.8 ns / instruction. 48.8/12.5 = 3.91 clock cycles / instruction.
  5) Assuming 80 MHz clock. Range: 0 to 209.715 ms. Resolution: 2 ^ 24. Precision: 12.5 ns (clock period).

Appendix A: Compiled Code for ISR

    78: void dummy(void){;}
0x00000968 4770 BX lr

    53: void Timer3A_Handler(void){
(2/8) 0x000007A4 B510 PUSH {r4,lr}
    54: PF2 ^= BLUE;
(1) 0x000007A6 480E LDR r0,[pc,#56] ; @0x000007E0
(1) 0x000007A8 6900 LDR r0,[r0,#0x10]
(1) 0x000007AA F0800004 EOR r0,r0,#0x04
(1) 0x000007AE 490C LDR r1,[pc,#48] ; @0x000007E0
(1) 0x000007B0 6108 STR r0,[r1,#0x10]
    55: PF2 ^= BLUE;
(1) 0x000007B2 4608 MOV r0,r1
(1) 0x000007B4 6900 LDR r0,[r0,#0x10]
(1) 0x000007B6 F0800004 EOR r0,r0,#0x04
(1) 0x000007BA 6108 STR r0,[r1,#0x10]
    56: TIMER3_ICR_R = TIMER_ICR_TATOCINT;// acknowledge TIMER3A timeout
(1) 0x000007BC 2001 MOVS r0,#0x01
(1) 0x000007BE 4909 LDR r1,[pc,#36] ; @0x000007E4
(1) 0x000007C0 6248 STR r0,[r1,#0x24]
    57: count++;
(1) 0x000007C2 4809 LDR r0,[pc,#36] ; @0x000007E8
(1) 0x000007C4 6800 LDR r0,[r0,#0x00]
(1) 0x000007C6 1C40 ADDS r0,r0,#1
(1) 0x000007C8 4907 LDR r1,[pc,#28] ; @0x000007E8
(1) 0x000007CA 6008 STR r0,[r1,#0x00]
    58: (*PeriodicTask)(); // execute user task
(1) 0x000007CC 4807 LDR r0,[pc,#28] ; @0x000007EC
(1) 0x000007CE 6800 LDR r0,[r0,#0x00]
(3) 0x000007D0 4780 BLX r0
    59: PF2 ^= BLUE;
(1) 0x000007D2 4803 LDR r0,[pc,#12] ; @0x000007E0
(1) 0x000007D4 6900 LDR r0,[r0,#0x10]
(1) 0x000007D6 F0800004 EOR r0,r0,#0x04
(1) 0x000007DA 4901 LDR r1,[pc,#4] ; @0x000007E0
(1) 0x000007DC 6108 STR r0,[r1,#0x10]
    60: }
(6/12) 0x000007DE BD10 POP {r4,pc}

Appendix B: Oscilloscope Images Measuring ISR Time